## Slide 1
DATA ACQUISITION, PROCESSING, AND INTERPRETATION OF A SINGLE-CHANNEL SURFACE ELECTROMYOGRAPHIC SENSOR WITH MACHINE LEARNING FOR THE SMART WEARABLE THERAPEUTIC GLOVE
Author: Alexander Ehrich Zapardiel
BSc in Electronic, Industrial, and Automatic Control Engineering
Advisor: Herminio Martínez García
Co-Advisor: Maziar Ahmadi Zeidabadi
Notes: https://pixabay.com/en/achievement-agreement-business-3481967/

## Slide 2: Thesis Presentation Outline
Introduction
Data Acquisition
Data Processing & Interpretation
Data Classification
Results
Conclusions & Future Improvements
01.
02.
03.
04.
05.
06.
Notes: https://pixabay.com/en/books-science-shelf-library-book-408220/

## Slide 3: Introduction
01
Motivation
Personal challenge
First AI steps
02
Scope
Electromyography
  Hardware & Firmware
  Data Acquisition
Machine Learning
  Software
  Data Processing
  Data Interpretation
  Data Classification
03
Targets
Own data acquisition process
Real-time data storing
Process the obtained data
Design different ML classification models and compare them
3

## Slide 4: Data Acquisition: Hardware & Firmware
ESP32 (2)
Wi-Fi module
Bluetooth module
VCC: 3.3 and 5 V
ADC resolution: 8 bit
sEMG sensor (1)
Output range: ±1,64 mV
VCC: 3V
4
Sources:
[1] pluxbiosignals.com
[2] leantec.es
01. Initialising
02. Connection to Wi-Fi & Firebase
03. Reading data
04. Sending data

## Slide 5: Data Acquisition: Hand-wrist gestures
Radial carpal extensor (1)
IN+
IN-
REF
Sources:
[1] Kenhub.com
5
Chosen gestures

## Slide 6: Data Acquisition: Measuring process
01
Prepare patient (electrodes & explain process)
02
03
04
6
1 patient = 3000 data values
Total patients = 90000 data values
Run code & acquisition starts
Repeat process 3 times per arm
Finish and remove electrodes
1 repetition = 100 data values
Resting period
Activation period
Resting period
1 gesture/patient = 600 data values
Rep. 1
Rep. 2
Rep. 3
Rep. 4
Rep. 5
Rep. 6

## Slide 7: Data Processing & Interpretation
7
1
2

## Slide 8: Data Processing & Interpretation
8
3
4

## Slide 9: Data Processing & Interpretation
9
5

## Slide 10: Data Processing & Interpretation
MAX1,1
MAX2,1
MAX3,1
MIN4,1
MIN5,1
Rep. 1
Rep. 2
Rep. 3
Rep. 4
MAX1,2
MAX2,2
MAX3,2
MIN4,2
MIN5,2
Sampling data in 2 parts
10
MAV, MAX, MIN
RMS, VAR
DAMV, DVARV, IASD, IE
Features

## Slide 11: Data Processing & Interpretation
Correlation Matrix from sampled data in 2
11

## Slide 12: Data Classification
Source:
[1] scikit-learn.org
2
3
1
Logistic Regression
12

## Slide 13: Data Classification
Source:
[1] medium.com
80% Training 20% Test
67% Training 33% Test
Train-Test Split
Model Accuracy
(Test Accuracy)
13
(1)

## Slide 14: Results
Efficiency and Accuracy Evaluators
1. Training Accuracy
2. Classification Report
3. Confusion Matrix
14

## Slide 15: Results
Implementation & Final Results Comparison
 | Logistic Regression |  | SVC |  | KNN | 
Test-size | 20% | 33% | 20% | 33% | 20% | 33%
Test Accuracy (%) | 60,80 | 55,52 | 57,95 | 54,83 | 51,70 | 51,03
Train Accuracy (%) | 56,13 | 56,12 | 62,11 | 61,56 | 64,39 | 62,76
Accuracy Gap (%) | 4,67 | 0,60 | 4,16 | 6,73 | 12,69 | 11,73
Classification Report |  | Test-size |  |  |  |  |  |  |  |  | 
 |  | 20% |  |  |  |  | 33% |  |  |  | 
Gesture |  | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 4 | 5
Logistic Regression | Precision | 0,90 | 0,44 | 0,54 | 0,59 | 0,52 | 0,89 | 0,37 | 0,49 | 0,47 | 0,49
 | Recall | 0,97 | 0,34 | 0,48 | 0,47 | 0,76 | 0,93 | 0,28 | 0,39 | 0,47 | 0,68
 | F1-score | 0,93 | 0,39 | 0,51 | 0,53 | 0,62 | 0,91 | 0,32 | 0,43 | 0,47 | 0,57
SVC | Precision | 0,91 | 0,38 | 0,50 | 0,56 | 0,49 | 0,93 | 0,31 | 0,55 | 0,43 | 0,52
 | Recall | 0,89 | 0,23 | 0,42 | 0,57 | 0,76 | 0,86 | 0,21 | 0,31 | 0,60 | 0,75
 | F1-score | 0,90 | 0,29 | 0,46 | 0,57 | 0,60 | 0,89 | 0,25 | 0,39 | 0,50 | 0,61
KNN | Precision | 0,94 | 0,40 | 0,26 | 0,59 | 0,44 | 0,96 | 0,37 | 0,29 | 0,43 | 0,52
 | Recall | 0,92 | 0,46 | 0,32 | 0,42 | 0,44 | 0,92 | 0,46 | 0,27 | 0,40 | 0,50
 | F1-score | 0,93 | 0,43 | 0,29 | 0,49 | 0,44 | 0,94 | 0,41 | 0,28 | 0,42 | 0,51
15
Implementation

## Slide 16: Conclusions & Future Improvements
16
Good quality and quantity of data are a must
Pre-processing the signal is vital for good quality features
First experience and project on this topic, helped to decide my next professional steps
01
More Data
02
Multi-Channel sEMG
03
Own Signal Monitoring
04
Deep Learning

## Slide 17
Thanks for your attention.
Notes: You can safely remove this slide. This slide design was provided by SlideModel.com – You can download more templates, shapes and elements for PowerPoint from http://slidemodel.com

## Slide 18
MAV: Mean Absolute Value (for each segment).
MAX: Maximum value for each segment.
MIN: Minimum value for each segment.
RMS: Quadratic mean of each segment.
VAR: Variance, to obtain the dispersion of the data points from the mean of the segment.
DAMV: Difference Absolute Mean Value, average absolute difference of two consecutive values of the signal divided by the length of the segment.
DVARV: Difference Variance Version, calculates the variance but applying the concept of the DAMV of calculating the difference between a value and its following.
IASD: Integrated Absolute of Second Derivative, calculates the relative change of the second derivative of the signal.
IE: Integrated Exponential, this feature amplifies large values and to suppresses the small ones by calculating the summation of the exponential value of the signal data values of the segment.
Features

## Slide 19: Data Processing & Interpretation
Correlation Matrix from original data

## Slide 20: Data Processing & Interpretation
Correlation Matrix from sampled data in 4

## Slide 21: Data Classification
2
3
1
Logistic Regression
Support Vector Classifier
K-Nearest Neighbours
[1]
[2]
[3]
Chosen ML Classification Models

## Slide 22: Results
First Results Comparison
 | Logistic Regression |  | SVC |  | KNN | 
Test-size | 20% | 33% | 20% | 33% | 20% | 33%
Test Accuracy (%) | 50,56 | 53,54 | 50,00 | 49,49 | 48,33 | 49,16
Train Accuracy (%) | 54,46 | 53,07 | 54,18 | 53,24 | 66,30 | 65,39
Accuracy Gap (%) | 3,90 | 0,47 | 4,18 | 3,75 | 17,97 | 16,23
Classification Report |  | Test-size |  |  |  |  |  |  |  |  | 
 |  | 20% |  |  |  |  | 33% |  |  |  | 
Gesture |  | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 4 | 5
Logistic Regression | Precision | 0,76 | 0,52 | 0,26 | 0,47 | 0,42 | 0,75 | 0,60 | 0,40 | 0,50 | 0,40
 | Recall | 0,91 | 0,37 | 0,17 | 0,50 | 0,62 | 0,93 | 0,44 | 0,21 | 0,55 | 0,61
 | F1-score | 0,83 | 0,43 | 0,20 | 0,48 | 0,50 | 0,83 | 0,50 | 0,28 | 0,52 | 0,48
SVC | Precision | 0,88 | 0,58 | 0,33 | 0,48 | 0,36 | 0,84 | 0,83 | 0,46 | 0,34 | 0,36
 | Recall | 0,80 | 0,16 | 0,17 | 0,78 | 0,71 | 0,84 | 0,08 | 0,18 | 0,74 | 0,75
 | F1-score | 0,84 | 0,25 | 0,22 | 0,60 | 0,48 | 0,84 | 0,14 | 0,26 | 0,54 | 0,49
KNN | Precision | 0,89 | 0,41 | 0,24 | 0,45 | 0,45 | 0,87 | 0,39 | 0,26 | 0,43 | 0,46
 | Recall | 0,91 | 0,49 | 0,25 | 0,47 | 0,29 | 0,93 | 0,42 | 0,18 | 0,49 | 0,48
 | F1-score | 0,90 | 0,45 | 0,24 | 0,46 | 0,36 | 0,90 | 0,40 | 0,21 | 0,46 | 0,47

## Slide 23: Realtime Evaluation
Signal Recording
Importing Signal
Signal Pre-processing
Features extraction
Classification Model
Output

## Slide 24: Realtime Evaluation

## Slide 25: Future Improvements
01
Increase dataset to improve the accuracy of the model.
More Data
02
Use a sensor with different channels to gain precision when it comes to define gestures.
Multi-Channel sEMG
03
An ADC with higher resolution is reflected in a cleaner signal, with less noise and more defined.
Higher ADC resolution
04
Create app that stores and monitors the data as all the fabricants do.
Own Signal Monitoring
05
Improve the actual process to reduce the acquisition time and increase the amount of data.
Different Data Acquisition
06
Use Deep Learning to implement a NN and improve the model.
Deep Learning